## Slide 1: ICCAD-2017 CAD Contest for Multi-Deck Standard Cell Legalization: Problem Description, Benchmarks, and Results
Ismail Bustany
Nima Karimpour Darav
Andrew Kennings
Notes: v

## Slide 2: Outline
Problem Description & Challenges
Multi-Deck Cell Legalization Problem Constraints
Evaluation Metrics
Benchmark Design Suites
Contest Results
Team Videos
The Winners

## Slide 3: Problem Description & Challenges
Notes: So what are the main challenges in legalization?

## Slide 4: A Sample of Multi-Deck Cells
vdd pin
vss pin
1-deck 2-deck 3-deck 4-deck
We used 1-4 deck high cells in the contest.
In advanced technology node real designs, it is common to common to see 2, 3, 4, 8, 16, 32-deck highcells.

## Slide 5: Motivation: Why use multi-deck cells?
Multi-deck cells (e.g. multi-bit registers (MBR’s)) are becoming more prevalent in advanced technology nodes (1-10% of cells) since they can improve PPA:
Lower Power: Fewer number of clock sinks seen by the clock-tree synthesis tool means less overall capacitance driven by the clock net.
Improve Performance: Shared logic (in clock gating or set-reset logic) and internally timing optimized MBR’s from a library team.
Lower clock skew in sequential gates: clock paths in MBR’s are internally balanced.
Smaller Area Utilization: Total number of clock buffers needed can be reduced.
https://www.embedded.com/design/mcus-processors-and-socs/4433619/2/Using-multi-bit-flip-flop-custom-cells-to-achieve-better-SoC-design-efficiency

## Slide 6: Traditional Single-Deck Legalization Requirements
Remove cell overlaps.
Minimally perturb incoming placed netlist to preserve (or improve) WL, routing, and timing quality metrics.
Satisfy complex design rules.
Fast and robust to handle large number of cells in state-of-the-art designs.

## Slide 7: Multi-Deck Standard Cell Legalization Requirements
Remove cell overlaps.
Minimally perturb incoming placed netlist to preserve (or improve) WL, routing, and timing quality metrics.
Satisfy complex design rules.
Fast and robust to handle large number of cells in state-of-the-art designs.
Plus,
Mixed-size cell legalization problem.

## Slide 8: Multi-Deck Standard Cell Legalization Problem
Movable cells
Blocked area
C
1
C
2
C4
C
5
C
6
C2
C8
C6
C
1
C
2
C
3
C4
C
5
C
6
C7
C7
A mixed-size legalization problem.
More challenging to model than the standard single-deck cell legalization problem.
Akin to an NP-hard multi-commodity network flow/Assignment problem.
C8
C3
Notes: Legalization is a step to mainly remove overlaps between cells and align cells with rows while considering additional constraints.

## Slide 9: Standard Cell Legalization Challenges
Legalization
Routability
Wire Length
Timing closure
Robust
Runtime
Complex Design Rules
Notes: With shrinking the size of transistors, complicated rules and multi-deck cells have become prevalent, The legalization process should address these two issues as well.

## Slide 10: Multi-Deck Standard Cell Legalization Challenges
Legalization
Routability
Wire Length
Timing closure
Robust
Runtime
Complex
Design Rules
Mixed sized Cells
Notes: With shrinking the size of transistors, complicated rules and multi-deck cells have become prevalent, The legalization process should address these two issues as well.

## Slide 11: Contest Legalization Problem Constraints
Notes: So what are the main challenges in legalization?

## Slide 12: Hard Constraints for the contest
P/G alignment
Row and site alignment.
Fence regions.
30 minute timeout.
Maximum 8 threads per run.

## Slide 13: P/G Alignment

## Slide 14: Fence Region Constraints

## Slide 15: Soft Constraints for the Contest
Target Area Utilization
Maximum cell movement objective
Detailed routing constraints
        - Cell spacing, pin access and shorts.

## Slide 16: Challenges – Edge Spacing Constraints
Two cells are too close to each other
Prone to pin access and short problems
Notes: Edge spacing rules are a minimum space between two or more objects. In this example, the shown two cells are too close to each other, therefore, the pins in pink are prone to pin access or short problems

## Slide 17: Evaluation Metrics
Notes: So what are the main challenges in legalization?

## Slide 18: Evaluation Metrics
The score of a solution is computed based on 5 metrics:
  Maximum cell movement - penalized by the maximum movement specific for the design.
  Average cell movement
  HPWL - penalized by the maximum utilization defined for the design.
  Runtime
  Detailed routing rule violations

## Slide 19: Total Design Score
Where

## Slide 20: Maximum Cell Movement Score
Where
Mi

## Slide 21: Average Movement Score
Where

## Slide 22: HPWL Score
Where

## Slide 23: Runtime Score
Where
for given team

## Slide 24: Soft Detailed Routing Score
Where

## Slide 25: Benchmark Design Suites
Notes: So what are the main challenges in legalization?

## Slide 26: Benchmark Format
cells.lef includes the physical characteristics of the technology library for the standard cell library, macros, and IO cells, etc.
tech.lef provides the physical characteristics of the routing layers, Vertical Interconnect Accesses (VIAs), placement site types, etc.
design.def includes design-specific logical and physical such as net-list connectivity, grouping information, physical constraints, cell locations and orientations, routing geometry data, P/G mesh, etc.
placement.constraints is a text file including some other constraints such as maximum target utilization or the maximum displacement. Any constraint defined in this file is considered a soft constraint.

## Slide 27: Benchmark Design Suites
The designs were created from the ISPD 2014 and 2015 Placement Contest benchmarks.
The global placements were generated by Eh?Placer.
Two sets of benchmarks were used for the final evaluation results:
- Released design suite includes 8 designs provided for the participants.
- Hidden design suite includes 8 designs used for blind evaluation.
- Both suites were equally weighted for the final evaluation
If a team could not generate a legal placement in a specified time (30 mins), the respective score is set to 1+e6.

## Slide 28: Released Benchmark Suite
Design | #Rows | #Macros | #Cells | #Nets | #Fence Regions | #I/O | % cell types |  |  |  | utilization
 |  |  |  |  |  |  | 1xH | 2xH | 3xH | 4xH | 
des_perf_b_md1 | 300 | 0 | 112679 | 122951 | 12 | 374 | 94.8 | 5.2 | 0 | 0 | 54.98
des_perf_b_md2 | 300 | 0 | 112679 | 122951 | 12 | 374 | 90.47 | 6.02 | 2.01 | 1.5 | 64.69
edit_dist_1_md1 | 361 | 0 | 130661 | 133223 | 0 | 2574 | 90.31 | 6.12 | 2.04 | 1.53 | 67.47
edit_dist_a_md2 | 400 | 6 | 127414 | 134051 | 1 | 2574 | 90.31 | 6.12 | 2.04 | 1.53 | 59.42
fft_2_md2 | 171 | 0 | 32281 | 33307 | 0 | 3010 | 89.62 | 6.56 | 2.18 | 1.64 | 83.12
fft_a_md2 | 400 | 6 | 30625 | 32090 | 0 | 3010 | 89.57 | 6.59 | 2.19 | 1.65 | 32.41
fft_a_md3 | 400 | 6 | 30625 | 32090 | 0 | 3010 | 93.42 | 2.19 | 2.19 | 2.19 | 31.24
pci_bridge32_a_md1 | 200 | 4 | 29533 | 34058 | 3 | 361 | 90.39 | 6.07 | 2.02 | 1.52 | 49.57

## Slide 29: Hidden Benchmark Suite
Design | #Rows | #Macros | #Cells | #Nets | #Fence Regions | #I/O | % cell types |  |  |  | utilization
 |  |  |  |  |  |  | 1xH | 2xH | 3xH | 4xH | 
des_perf_1 | 222 | 0 | 112644 | 112880 | 0 | 374 | 100.00 | 0.00 | 0.00 | 0.00 | 90.64
des_perf_a_md1 | 450 | 4 | 103589 | 115187 | 4 | 374 | 95.66 | 4.34 | 0.00 | 0.00 | 55.11
des_perf_a_md2 | 450 | 4 | 103589 | 115187 | 4 | 374 | 96.99 | 1.00 | 1.00 | 1.00 | 55.92
edit_dist_a_md3 | 400 | 6 | 119626 | 134051 | 1 | 2574 | 93.88 | 2.04 | 2.04 | 2.04 | 57.22
pci_bridge32_a_md2 | 200 | 4 | 29533 | 34058 | 3 | 361 | 85.51 | 7.08 | 4.04 | 3.37 | 57.72
pci_bridge32_b_md1 | 400 | 6 | 26134 | 32546 | 3 | 361 | 90.38 | 6.07 | 2.02 | 1.52 | 28.68
pci_bridge32_b_md2 | 400 | 6 | 26134 | 32546 | 3 | 362 | 97.97 | 1.01 | 1.01 | 1.01 | 19.72
pci_bridge32_b_md3 | 400 | 6 | 26134 | 32546 | 3 | 363 | 94.94 | 1.01 | 2.02 | 2.02 | 23.98

## Slide 30: Contest Results
Notes: So what are the main challenges in legalization?

## Slide 31: Teams
11 final submissions from Brazil, China, Germany, Hong Kong, Taiwan, and the USA.
8 out of 11 teams could generate at least one legal solution.
The ranking was significantly impacted by the number of legal solutions generated by the teams.
Notes: In summary, our proposed algorithm results in less maximum and average cell movement. In addition, the proposed method is scalable and robust with respect to the floorplan complexity and number of cells in designs.

## Slide 32: Released Suite Scores
cada005, cada012, cada040, cada041, and cada053 generated legal solutions for all designs of the released suite within the 30-min allotted time.
Team | Score | #Failures
cada001 | 100018.68 | 1
cada005 | 10.50 | 0
cada006 | 800000.00 | 8
cada012 | 4.86 | 0
cada021 | 800000.00 | 8
cada036 | 800000.00 | 8
cada040 | 9.22 | 0
cada041 | 7.64 | 0
cada045 | 100008.20 | 1
cada053 | 6.75 | 0
cada099 | 800000.00 | 8

## Slide 33: Hidden Suite Scores
Only two teams generated legal solutions for all designs in the suite within the allotted 30-min time
Team | Score | #Failures
TBA | 6913.44 | 0
TBA | 201640.75 | 2
TBA | 800000.00 | 8
TBA | 117.34 | 0
TBA | 800000.00 | 8
TBA | 800000.00 | 8
TBA | 512841.70 | 4
TBA | 100762.61 | 1
TBA | 700001.07 | 7
TBA | 600001.75 | 6
TBA | 718655.40 | 7

## Slide 34: And Now, Introducing the Top 6 Winning Teams!

## Slide 35: The Winners!
Notes: So what are the main challenges in legalization?

## Slide 36: Released Benchmark Scores (runtime adjusted)
Team | des_perf_b_md1 |  |  | des_perf_b_md2 |  |  | edit_dist_1_md1 |  |  | edit_dist_a_md2 |  | 
 | Raw Score | Runtime | Scaled Score | Raw Score | Runtime | Scaled Score | Raw Score | Runtime | Scaled Score | Raw Score | Runtime | Scaled Score
cada001 | 100000.00 | -- | 100000.00 | 0.88 | 4.80 | 0.82 | 11.55 | 5.14 | 10.71 | 4.42 | 4.79 | 4.07
cada005 | 1.32 | 9.34 | 1.31 | 1.52 | 23.23 | 1.59 | 1.23 | 25.00 | 1.28 | 1.22 | 27.07 | 1.27
cada012 | 0.63 | 6.59 | 0.61 | 0.72 | 6.26 | 0.68 | 0.73 | 8.58 | 0.70 | 0.53 | 7.59 | 0.50
cada040 | 1.05 | 34.28 | 1.13 | 0.97 | 56.47 | 1.07 | 1.58 | 67.10 | 1.76 | 0.74 | 108.00 | 0.84
cada041 | 1.27 | 10.85 | 1.27 | 0.92 | 18.01 | 0.94 | 0.82 | 20.60 | 0.84 | 0.78 | 31.50 | 0.83
cada045 | 100000.00 | -- | 100000.00 | 0.75 | 3.93 | 0.69 | 0.78 | 4.14 | 0.71 | 4.35 | 4.46 | 3.98
cada053 | 0.97 | 12.08 | 0.98 | 0.91 | 12.65 | 0.91 | 0.86 | 14.14 | 0.86 | 0.62 | 14.36 | 0.62
cada099 | 100000.00 | -- | 100000.00 | 100000.00 | -- | 100000.00 | 100000.00 | -- | 100000.00 | 100000.00 | -- | 100000.00
Team | fft_2_md2 |  |  | fft_a_md2 |  |  | fft_a_md3 |  |  | pci_bridge32_a_md1 |  | 
 | Raw Score | Runtime | Scaled Score | Raw Score | Runtime | Scaled Score | Raw Score | Runtime | Scaled Score | Raw Score | Runtime | Scaled Score
cada001 | 1.06 | 1.08 | 0.95 | 0.63 | 1.13 | 0.58 | 0.50 | 1.11 | 0.47 | 1.14 | 1.24 | 1.08
cada005 | 2.01 | 6.34 | 2.06 | 0.70 | 4.03 | 0.71 | 0.56 | 3.30 | 0.57 | 1.64 | 4.51 | 1.71
cada012 | 0.79 | 1.60 | 0.74 | 0.53 | 1.41 | 0.50 | 0.42 | 1.36 | 0.39 | 0.76 | 1.43 | 0.73
cada040 | 1.81 | 27.42 | 2.05 | 0.61 | 5.07 | 0.64 | 0.47 | 4.53 | 0.49 | 1.15 | 7.40 | 1.24
cada041 | 1.47 | 30.64 | 1.68 | 0.53 | 2.50 | 0.52 | 0.41 | 2.45 | 0.41 | 1.15 | 2.51 | 1.15
cada045 | 1.01 | 0.93 | 0.90 | 0.56 | 11.53 | 0.62 | 0.43 | 10.39 | 0.47 | 0.90 | 0.94 | 0.84
cada053 | 1.21 | 4.35 | 1.21 | 0.63 | 3.16 | 0.63 | 0.49 | 2.95 | 0.49 | 1.05 | 2.75 | 1.05
cada099 | 100000.00 | -- | 100000.00 | 100000.00 | -- | 100000.00 | 100000.00 | -- | 100000.00 | 100000.00 | -- | 100000.00

## Slide 37: Hidden Benchmark Scores (runtime adjusted)
Rank | TEAM | des_perf_b_md1 |  |  | des_perf_b_md2 |  |  | edit_dist_1_md1 |  |  | edit_dist_a_md2 |  | 
 |  | Raw Score | Runtime (sec) | Score with runtime | Raw Score | Runtime (sec) | Score with runtime | Raw Score | Runtime (sec) | Score with runtime | Raw Score | Runtime (sec) | Score with runtime
1 | cada053 | 0.93 | 14.84 | 0.93 | 0.87 | 15.39 | 0.87 | 0.80 | 17.42 | 0.80 | 0.64 | 21.02 | 0.64
2 | cada012 | 0.79 | 8.27 | 0.75 | 0.85 | 9.35 | 0.82 | 1.66 | 11.93 | 1.61 | 0.69 | 12.10 | 0.66
3 | cada005 | 2.36 | 52.83 | 2.57 | 3.97 | 35.62 | 4.21 | 4.92 | 38.19 | 5.20 | 1.99 | 39.84 | 2.09
- | cada040 | Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | --
- | cada001 | Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | --
- | cada099 | Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | --
fft_2_md2 |  |  | fft_a_md2 |  |  | fft_a_md3 |  |  | pci_bridge32_a_md1 |  |  | Total Scores | 
Raw Score | Runtime (sec) | Score with runtime | Raw Score | Runtime (sec) | Score with runtime | Raw Score | Runtime (sec) | Score with runtime | Raw Score | Runtime (sec) | Score with runtime | Raw Score | with Runtime
0.95 | 4.02 | 0.95 | 0.58 | 6.42 | 0.58 | 0.45 | 6.35 | 0.45 | 1.00 | 3.90 | 1.00 | 6.22 | 6.22
1.24 | 2.47 | 1.19 | 0.57 | 1.83 | 0.51 | 0.44 | 1.79 | 0.40 | 1.01 | 1.58 | 0.94 | 7.23 | 6.89
2.98 | 7.21 | 3.10 | 1.99 | 8.49 | 2.04 | 3.03 | 8.50 | 3.10 | 3.30 | 8.38 | 3.48 | 24.55 | 25.79
Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | -- | -- | --
Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | -- | -- | --
Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | -- | -- | --
Rank | TEAM | des_perf_b_md1
1 | cada053 | 
2 | cada012 | 
3 | cada005 | 
- | cada040 | 
- | cada001 | 
- | cada099 | 

## Slide 38: Impact of Hidden Benchmark on Final Scores
Only two teams, cada001 and cada012, could generate legal solutions for all 8 designs within the allotted time (30 min).
The runtime for some legalizers was significantly affected by the maximum movement constraints. This was especially deleterious for teams cada040 and cada053’s final scores.
Team cada012 performed best on these benchmarks.
Team | Score | #Failures
cada001 | 6913.44 | 0
cada005 | 201640.75 | 2
cada006 | 800000.00 | 8
cada012 | 117.34 | 0
cada021 | 800000.00 | 8
cada036 | 800000.00 | 8
cada040 | 512841.70 | 4
cada041 | 100762.61 | 1
cada045 | 700001.07 | 7
cada053 | 600001.75 | 6
cada099 | 718655.40 | 7

## Slide 39: Top 6 Teams
1st place: 122.20
2nd place: 100770.25
3rd place: 106932.12
4th place: 201651.26
5th place: 512850.92
6th place: 600008.51
39

## Slide 40: Honorable Mention 
Team cada053: RippleLG
The Chinese University of Hong Kong
Hong Kong
Haocheng Li, Wing-Kai Chow, Gengjie Chen,
Prof. Evangeline F. Y. Young, Prof. Bei Yu

## Slide 41: Honorable Mention 
Team cada040: TU Dresden
Dresden University of Technology
Germany
Tilman Horst, Andreas Krinke, Steve Bigalke, Robert Fischbach,
Arthur Nothdurft, Sergii Osmolovskyi, Mohamed Sabra, Matthias Thiele,
Prof. Jens Lienig

## Slide 42: Honorable Mention 
Team cada005: NCKU_95416
National Cheng Kung University
Taiwan
Tai-Ting Chen, You-Lun Deng, Yi-Wen Wang, Prof. Jai-Ming Lin

## Slide 43: 3rd Place 
Team cada001: Ophidian
Federal University of Santa Catarina
Brazil
Renan Netto, Tiago Augusto Fontana, Sheiny Fabre,
Thiago Barbato, Chrystian Guth,
Prof. Jose Luis Guntzel, Prof. Laercio Lima Pilla

## Slide 44: 2nd Place 
Team cada041: ColdNoodle
National Taiwan University
Taiwan
Shih-Wei Hsieh, Shao-Chun Hung
Prof. Yao-Wen Chang

## Slide 45: 1st Place 
Team cada012: C_TI
Fuzhou University
China
Ziran Zhu, Yuhang Chen, Ye Huang, Xingquan Li,
Prof. Jianli Chen, Prof. Wenxing Zhu, Prof. Genghua Fan

## Slide 46: Released Benchmark Scores (runtime adjusted)
Team | des_perf_b_md1 |  |  | des_perf_b_md2 |  |  | edit_dist_1_md1 |  |  | edit_dist_a_md2 |  | 
 | Raw Score | Runtime | Scaled Score | Raw Score | Runtime | Scaled Score | Raw Score | Runtime | Scaled Score | Raw Score | Runtime | Scaled Score
cada001 | 100000.00 | -- | 100000.00 | 0.88 | 4.80 | 0.82 | 11.55 | 5.14 | 10.71 | 4.42 | 4.79 | 4.07
cada005 | 1.32 | 9.34 | 1.31 | 1.52 | 23.23 | 1.59 | 1.23 | 25.00 | 1.28 | 1.22 | 27.07 | 1.27
cada012 | 0.63 | 6.59 | 0.61 | 0.72 | 6.26 | 0.68 | 0.73 | 8.58 | 0.70 | 0.53 | 7.59 | 0.50
cada040 | 1.05 | 34.28 | 1.13 | 0.97 | 56.47 | 1.07 | 1.58 | 67.10 | 1.76 | 0.74 | 108.00 | 0.84
cada041 | 1.27 | 10.85 | 1.27 | 0.92 | 18.01 | 0.94 | 0.82 | 20.60 | 0.84 | 0.78 | 31.50 | 0.83
cada045 | 100000.00 | -- | 100000.00 | 0.75 | 3.93 | 0.69 | 0.78 | 4.14 | 0.71 | 4.35 | 4.46 | 3.98
cada053 | 0.97 | 12.08 | 0.98 | 0.91 | 12.65 | 0.91 | 0.86 | 14.14 | 0.86 | 0.62 | 14.36 | 0.62
cada099 | 100000.00 | -- | 100000.00 | 100000.00 | -- | 100000.00 | 100000.00 | -- | 100000.00 | 100000.00 | -- | 100000.00
Team | fft_2_md2 |  |  | fft_a_md2 |  |  | fft_a_md3 |  |  | pci_bridge32_a_md1 |  | 
 | Raw Score | Runtime | Scaled Score | Raw Score | Runtime | Scaled Score | Raw Score | Runtime | Scaled Score | Raw Score | Runtime | Scaled Score
cada001 | 1.06 | 1.08 | 0.95 | 0.63 | 1.13 | 0.58 | 0.50 | 1.11 | 0.47 | 1.14 | 1.24 | 1.08
cada005 | 2.01 | 6.34 | 2.06 | 0.70 | 4.03 | 0.71 | 0.56 | 3.30 | 0.57 | 1.64 | 4.51 | 1.71
cada012 | 0.79 | 1.60 | 0.74 | 0.53 | 1.41 | 0.50 | 0.42 | 1.36 | 0.39 | 0.76 | 1.43 | 0.73
cada040 | 1.81 | 27.42 | 2.05 | 0.61 | 5.07 | 0.64 | 0.47 | 4.53 | 0.49 | 1.15 | 7.40 | 1.24
cada041 | 1.47 | 30.64 | 1.68 | 0.53 | 2.50 | 0.52 | 0.41 | 2.45 | 0.41 | 1.15 | 2.51 | 1.15
cada045 | 1.01 | 0.93 | 0.90 | 0.56 | 11.53 | 0.62 | 0.43 | 10.39 | 0.47 | 0.90 | 0.94 | 0.84
cada053 | 1.21 | 4.35 | 1.21 | 0.63 | 3.16 | 0.63 | 0.49 | 2.95 | 0.49 | 1.05 | 2.75 | 1.05
cada099 | 100000.00 | -- | 100000.00 | 100000.00 | -- | 100000.00 | 100000.00 | -- | 100000.00 | 100000.00 | -- | 100000.00

## Slide 47: Hidden Benchmark Scores (runtime adjusted)
Rank | TEAM | des_perf_b_md1 |  |  | des_perf_b_md2 |  |  | edit_dist_1_md1 |  |  | edit_dist_a_md2 |  | 
 |  | Raw Score | Runtime (sec) | Score with runtime | Raw Score | Runtime (sec) | Score with runtime | Raw Score | Runtime (sec) | Score with runtime | Raw Score | Runtime (sec) | Score with runtime
1 | cada053 | 0.93 | 14.84 | 0.93 | 0.87 | 15.39 | 0.87 | 0.80 | 17.42 | 0.80 | 0.64 | 21.02 | 0.64
2 | cada012 | 0.79 | 8.27 | 0.75 | 0.85 | 9.35 | 0.82 | 1.66 | 11.93 | 1.61 | 0.69 | 12.10 | 0.66
3 | cada005 | 2.36 | 52.83 | 2.57 | 3.97 | 35.62 | 4.21 | 4.92 | 38.19 | 5.20 | 1.99 | 39.84 | 2.09
- | cada040 | Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | --
- | cada001 | Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | --
- | cada099 | Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | --
fft_2_md2 |  |  | fft_a_md2 |  |  | fft_a_md3 |  |  | pci_bridge32_a_md1 |  |  | Total Scores | 
Raw Score | Runtime (sec) | Score with runtime | Raw Score | Runtime (sec) | Score with runtime | Raw Score | Runtime (sec) | Score with runtime | Raw Score | Runtime (sec) | Score with runtime | Raw Score | with Runtime
0.95 | 4.02 | 0.95 | 0.58 | 6.42 | 0.58 | 0.45 | 6.35 | 0.45 | 1.00 | 3.90 | 1.00 | 6.22 | 6.22
1.24 | 2.47 | 1.19 | 0.57 | 1.83 | 0.51 | 0.44 | 1.79 | 0.40 | 1.01 | 1.58 | 0.94 | 7.23 | 6.89
2.98 | 7.21 | 3.10 | 1.99 | 8.49 | 2.04 | 3.03 | 8.50 | 3.10 | 3.30 | 8.38 | 3.48 | 24.55 | 25.79
Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | -- | -- | --
Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | -- | -- | --
Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | -- | Not legal | -- | -- | -- | --
Rank | TEAM | des_perf_b_md1
1 | cada053 | 
2 | cada012 | 
3 | cada005 | 
- | cada040 | 
- | cada001 | 
- | cada099 | 

## Slide 48: ICCAD-2017 CAD Contest for Multi-Deck Standard Cell Legalization: Problem Description, Benchmarks, and Results
Ismail Bustany
Nima Karimpour Darav
Andrew Kennings
Notes: v